## Slide 1
Workshop: Data Lake
CryoEM facility at UMG
Tat Cheng

## Slide 2
Titan Krios G4
Falcon4
4k x 4k physical pixel
250 frames/sec
EER format: x, y, t
oversampled 16k x 16k grid

## Slide 3
2 modes of data collection and processing: SPA

## Slide 4
EER size: ~400 – 700 Mb
Speed: ~300 images /hour
An overnight session: ~16 hours, 4800 images
Case 1: 960 Gb in 3 hours
Case 2: 3 Tb in 16 hours
Data size is the problem
Data collection (fast)
Data processing
Well established softwares
GPU powered
Size of output relatively small compared to input
Some downstream processing can/should be done locally

## Slide 5
2 modes of data collection and processing: Tomo

## Slide 6
Tilt series:
EER Size: ~150 – 400 Mb
Number of images: 43
Speed: ~45 mins
An overnight session: ~16 hours, 20 TS, 860 images
Case 1: 218 Gb in 8 hours
Data collection slow
Data processing
No well established software
GPU /CPU powered
Size of output relatively big compared to input
Size of each project varies
Data management is the problem

## Slide 7
Vis Server

## Slide 8
Acknowledgements
Prof. Ruben Busnadiego-Fernandez
Dr. Eri Sakata
..and all group members
The IT group
Tapu Shaikh
Dirk Schwitters
Tianming Yi
Kevin Sicking
Midea Ortiz Rios